## Slide 1: LH₂ stays above NH₃ on delivered cost through 2045 on almost every path, and none of the improvement is proven yet
Pure H₂ delivered at the import terminal gate, 100 kt/yr, 8,000 km, same production cost for both routes. Default view: LH₂ published targets met against improving NH₃.
Gap in 2026, LH₂ minus NH₃
$1.96
LH₂ $8.65 vs NH₃ $6.69 per kg
Gap in 2030
$1.53
LH₂ $7.37 vs NH₃ $5.83
Parity year on this path
Not by 2045
Gap in 2045: $0.10. Against flat NH₃: about 2039
Backed by operating evidence
0%
$2.08 of $2.08 per kg rests on grade D or E
Delivered cost, USD per kg H₂
Chart: 
| 2026 | 2030 | 2035 | 2040 | 2045
LH₂ (targets met) | 8.65 | 7.37 | 5.89 | 4.91 | 4.75
NH₃ (improving) | 6.69 | 5.83 | 5.26 | 4.8 | 4.65
How to read it
The gap narrows from $1.96 to $0.11 by 2040, then stalls.
Liquefier CAPEX and large LH₂ tanks carry the closure. Liquefaction energy carries very little.
Parity needs every target on schedule and NH₃ standing still.
Nothing past 2026 is a forecast. The years apply developers' own targets.
Sources: IEA GHR 2026 annex; KHI/NEDO roadmap; Incheon plant (Korea.net); HySTRA/Kawasaki; DOE; KBR/CATF. Model run on the published inputs in the register.
Notes: Default dashboard view. LH2 on the published-targets path against NH3 on the improving path. The 2026 gap is about USD 2 per kg. It narrows to roughly USD 0.1 per kg by 2040 and then stops closing. Against flat NH3 the paths cross around 2039. All the improvement beyond 2026 rests on inputs graded D or E: vendor claims, plans or assumptions.

## Slide 2: Where the cost sits, and which stages have not yet been shown to work at the scale assumed
Chart: 
| LH₂ 2026 $8.65 | NH₃ 2026 $6.69 | LH₂ 2030 $7.37 | NH₃ 2030 $5.83
Production (common LCOH) | 4 | 4 | 3.2 | 3.2
Hydrogen losses | 0.34 | 0.29 | 0.24 | 0.23
Conversion | 2.36 | 0.71 | 1.99 | 0.71
Export storage | 0.53 | 0.35 | 0.53 | 0.35
Shipping | 0.47 | 0.17 | 0.47 | 0.17
Import storage | 0.56 | 0.35 | 0.56 | 0.35
Reconversion | 0.39 | 0.82 | 0.39 | 0.82
Credibility by stage in 2030. Letter = evidence grade; shaded amber = scale not yet demonstrated
 | Conversion | Export storage | Shipping | Import storage | Reconversion
LH₂ | D Scale-up 1.7× 30 → 50 t/d | D Scale-up 13× 3,200 → 43,100 m³ | D Scale-up 36× 75 → 2,700 t H₂ | D Scale-up 15× 3,200 → 47,700 m³ | C Not assessed
NH₃ | A Established | A Established | B Established 63,200 → 63,200 t NH₃ | A Established | D Scale-up 40× 30 → 1,200 t NH₃/d
Scale-up is the size needed divided by the largest size demonstrated. Sources: Incheon/Korea.net, HySTRA, DOE/NASA, Air Liquide, KHI, ADNOC L&S, IEA GHR 2026. Grades never rise because a date arrives.
Notes: Top: the stacked cost per kg delivered for each route in 2026 and 2030. Grey is the common production cost. Bottom: for 2030, how far each stage must scale beyond what has been demonstrated. LH2 needs a 50 t/d liquefier train against 30 t/d proven, a tank 13 times the largest operating, and a carrier many times larger than the 75 t pilot. NH3 shipping is established; the cracker needs about 40 times the pilot.

## Slide 3: Parity is conditional: about 2039 against flat NH₃, and not reached by 2045 in the other three cases
Gap, LH₂ minus NH₃, USD per kg (below zero = LH₂ cheaper)
Chart: 
| 2026 | 2030 | 2035 | 2040 | 2045
Targets met vs NH₃ flat | 1.96 | 1.53 | 0.49 | -0.17 | -0.23
Targets met vs NH₃ improving | 1.96 | 1.53 | 0.63 | 0.11 | 0.1
Conservative vs NH₃ flat | 1.96 | 1.82 | 1.34 | 0.77 | 0.67
Conservative vs NH₃ improving | 1.96 | 1.82 | 1.48 | 1.05 | 0.99
Parity year by path
Targets met vs NH₃ flat
About 2039
Gap in 2040 −$0.17, in 2045 −$0.23
Targets met vs NH₃ improving
Not by 2045
Gap in 2040 $0.11, in 2045 $0.10
Conservative vs NH₃ flat
Not by 2045
Gap in 2040 $0.77, in 2045 $0.67
Conservative vs NH₃ improving
Not by 2045
Gap in 2040 $1.05, in 2045 $0.99
Paths after 2026 apply published developer targets on a stated schedule; they are scenarios, not forecasts. Independent studies (KBR/CATF, arXiv 2025) find no parity before 2040.
Notes: Four combinations of the two LH2 paths and two NH3 paths. The only crossing is when every LH2 target is met on time and NH3 does not improve. If NH3 improves as modestly assumed, the paths stay within about USD 0.10 per kg through 2045. If LH2 delivers only half the improvement, the gap stays between 0.7 and 1.0.

## Slide 4: Every dollar of LH₂ improvement rests on a claim, a plan or an assumption, and none is yet operating evidence
Effect on the 2040 gap of each input, USD per kg
Chart: 
| LH₂: Liquefier CAPEX | LH₂: LH₂ tank cost | LH₂: Liquefaction energy | LH₂: Carrier size and price | LH₂: Boil-off | NH₃: Carrier size and price | NH₃: Cracker heat | NH₃: Cracker CAPEX
Gap effect | 0.83 | 0.8 | 0.17 | 0.16 | 0.11 | -0.05 | -0.08 | -0.16
Teal closes the gap (LH₂). Amber widens it (NH₃ improvements).
$2.08
per kg that technology inputs take off the LH₂ cost, 2026 to 2040 (one lever at a time)
0%
of it supported by operating evidence (grades A to C). The rest is grade D or E.
What would turn a claim into evidence
Measured energy of the KHI 50 t/d liquefier
KHI 50,000 m³ tank cost and boil-off
Published price and voyage data, 40,000 m³ carrier
Effects are one input at a time and do not add exactly. Grades: D vendor claim or plan, E study or assumption. Sources: KHI/NEDO, DOE AMR 2024, HySTRA, Maritime Optima, IEA GHR 2026.
Notes: Each bar reverts one input to its 2026 value and shows how much of the LH2 cost reduction disappears. Liquefier CAPEX and tank cost are about 0.8 dollars per kg each. Liquefaction energy, which gets the most attention, is only about 0.17. Every one of these inputs is a claim, plan or assumption today. The NH3 improvements are also assumptions and widen the gap.

## Slide 5: LH₂ tank cost alone moves the 2040 delivered cost by about $6 per kg, more than any other input
Delivered cost in 2040 by LH₂ tank cost, USD per kg
Chart: 
| LH₂, DOE/Shell concept tank (~$1,750/m³) | LH₂, IEA tank cost (~$9,000/m³) | LH₂, KBR tank cost (~$52,600/m³) | NH₃, improving path
Delivered | 4.85 | 5.71 | 10.84 | 4.8
KHI's 50,000 m³ Ogishima tank is the data point that would settle this. Its cost is unpublished.
One input changed, 2040 | LH₂ | NH₃ | Gap
Base case | $4.91 | $4.80 | $0.11
Liquefaction energy stays at the 2026 value | $5.08 | $4.80 | $0.27
Liquefaction energy 6 kWh/kg | $4.91 | $4.80 | $0.11
Liquefier CAPEX −25% | $4.65 | $4.80 | −$0.15
Liquefier CAPEX +50% | $5.43 | $4.80 | $0.63
LH₂ carrier CAPEX −30% | $4.82 | $4.80 | $0.02
Cracker CAPEX $1,900/t H₂/yr (study) | $4.91 | $4.82 | $0.09
Cracker heat 6.4 kWh/kg (KBR/CATF) | $4.91 | $4.75 | $0.16
Power price 60 USD/MWh | $5.04 | $4.91 | $0.14
Discount rate 10% | $5.15 | $5.00 | $0.15
Distance 12,000 km | $5.07 | $4.86 | $0.20
LH₂ targets met vs NH₃ improving. Tank anchors: IEA GHR 2026 annex, DOE/Shell/CB&I concept (DOE AMR 2024), KBR/CATF 2022. Cracker heat: IEA base 10.2 kWh/kg, KBR 6.4.
Notes: The three published tank costs differ by a factor of about thirty, from under 1,750 dollars per cubic metre in the DOE and Shell concept, to about 9,000 in the IEA annex, to about 52,600 for the 4,000 cubic metre tanks in the KBR study. That single input swings the 2040 LH2 cost between roughly 4.85 and 10.84 dollars per kg. The table shows the other sensitivities for the same year. KBR cracker heat of 6.4 kWh per kg is a sensitivity; the IEA 10.2 is the base.

## Slide 6: The evidence that would change the picture arrives between late 2026 and about 2038, and we can ask for it now
Route | Milestone | Date or target | Evidence to ask for
NH₃ | Uniper/Uhde 28 t NH₃/d cracker commissioning | End 2026 | Confirmed start-up and test results
LH₂ | KHI 50 t/d liquefier completes | End 2028 | Measured specific energy at 50 t/d
LH₂ | Ship-to-base transfer and ocean trials | FY2030 | Boil-off, transfer losses, reliability
LH₂ | KHI large compressor commercial launch (roadmap) | About 2031 | Operating compressor in a liquefier
LH₂ | KHI power-recovery and wet turbines (roadmap) | About 2035 | Demonstration units operating
LH₂ | KHI magnetic refrigeration commercial (roadmap) | About 2038 | Large-scale test
LH₂ | Korean consortium LH₂ carriers (40,000 and 160,000 m³) | 2032 to 2040 | Contract and price
NH₃ | First 175,000 m³ ammonia carriers (ADNOC L&S) | 2029 | Delivery
NH₃ | First cracker above 300 t NH₃/d in operation | No verified date | Operating plant with published data
Ask KHI
Cost and boil-off of the 50,000 m³ tank
Price and delivery of the 40,000 m³ carrier
Guaranteed energy of the 50 t/d liquefier
Ask Air Liquide
Guaranteed energy and CAPEX for a 60 to 150 t/d train
Performance data from the 30 t NH₃/d cracker pilot
Reference plants above 30 t/d single train
Developer targets, not commitments; several have slipped before. Sources: KHI (19 Oct 2026), KHI/NEDO roadmap, Kawasaki/JSE, Uniper/thyssenkrupp Uhde, ADNOC L&S, Baird Maritime.
Notes: The milestones are the points at which an input moves from a claim to operating evidence. The Uhde cracker demonstration is due at the end of this year. The KHI 50 t/d liquefier completes at the end of 2028 and the ship-to-base trials follow by FY2030. The asks on the right are what Gentari can request from the two vendors now.

## Slide 7: Independent studies agree LH₂ costs more, and the evidence base is mostly plans and assumptions
Register entries by grade
Chart: 
| Grade B | Grade D | Grade E
Entries | 11 | 12 | 9
32
entries
A Independent operating data (0)
B Company-reported operating data (11)
C Contractual guarantee (0)
D Vendor claim or plan (12)
E Study or assumption (9)
No entry is independent operating data (grade A).
Postures, paths and scale targets are analyst judgements for panel validation.
Independent study | Period | LH₂ | NH₃
KBR for CATF | 250 kt/yr 2030 | $6.09 | $3.25
KBR for CATF | 1,000 kt/yr 2040 | $4.64 | $2.57
KBR for CATF | 10,000 kt/yr 2050 | $3.23 | $1.96
IEA ETP 2023, transport only | 2030 | $2.0–3.7 | $1.9–2.2
arXiv 2507.02412 | 2030 | — | 16% edge
arXiv 2507.02412 | 2040 | — | 10% edge
Caveats to resolve before external use
KBR figures include blue-hydrogen production and are volume scenarios, not calendar years
Roland Berger "near parity by 2035" could not be verified and is excluded
KHI tank cost, carrier price and guaranteed liquefier energy are unpublished
Sources: KBR/CATF 2022, IEA ETP 2023 (via Hydrogen Insight), arXiv 2507.02412. Full register with grades, caveats and review dates is in the live dashboard.
Notes: Independent studies use different boundaries and none is a like-for-like match, but all place LH2 above cracked ammonia and none finds parity before 2040. The register behind the dashboard has 32 sourced entries, none of them independent operating data.