## Slide 1: LH2 Value Chain: Technology Database Syndication
Rev 0 · October 2026
Notes: Purpose: walk all departments through the LH2 Value Chain Technology Database, Rev 0 (18 Sep 2026): what it covers, the key numbers, and what is still open.

## Slide 2: The database is a single reference for the LH₂ chain, from the liquefier to hydrogen gas at the import terminal, in 13 sections
LiqH₂VC Database Rev 0 · scope and structure
Liquefaction
Export storage & loading
Shipping
Import & regasification
Properties, liquefaction cycles, technology players, plants built
Sections 1–5, 8.1, 10.1
Tank types, boil-off, export-terminal cost
Sections 6, 8.2, 10.2
LH₂ carriers, marine projects, road and rail, ship boil-off
Sections 7, 10.3, 12.2
Vaporisers and the receiving terminal
Sections 9, 10.4
Across the chain: Export-facility cost (8) · Regulation (11) · Key challenges (12) · LH₂ vs NH₃ as hydrogen carrier (13)
Boundary: gaseous hydrogen at the export plant to gaseous hydrogen at import send-out; producing the hydrogen is outside the database. Use: technology benchmarking, project screening and preliminary techno-economic assessment.
Rev 0, 18 Sep 2026. Prepared by Jasmin Suraya and Ungku M Zulhilmi Ungku Zakaria; reviewed by Wan M Ikhwan Wan Yussoff and Octavian Partenie; approved by Danial Khairi Ahmad; accepted by Alex Bower.
Notes: One document, four links in the chain plus four cross-cutting sections. Hydrogen production itself is outside the database.

## Slide 3: Cooling hydrogen to −253 °C makes it about 800 times more compact than the gas, which is what makes bulk shipping possible
LiqH₂VC Database Rev 0 · Sections 1.1 and 2.2 · properties of liquid hydrogen
−253 °C
Boiling point at atmospheric pressure (about 20.3 K)
70.8 kg/m³
Density of liquid hydrogen, against 0.0899 kg/m³ for the gas
~800×
Less storage volume than the gas at standard conditions
120 MJ/kg
Lower heating value, the highest per kilogram of any fuel
Ortho-para conversion drives boil-off
Room temperature
75 % ortho
25 % para
Liquid hydrogen
Nearly 100 % para
Ortho turns into para as hydrogen cools, and the change releases heat. If it happens in the tank, that heat boils off LH₂, so catalysts convert it stage by stage inside the liquefier.
Notes: Four numbers to remember. The ortho-para point explains why liquefiers include catalysts and why boil-off is never zero.

## Slide 4: Today's liquefiers use 10–13 kWh/kg H₂, about three times the 3.3 kWh/kg minimum; Kawasaki targets 8–9 now and 6 at large scale
LiqH₂VC Database Rev 0 · Sections 2.1, 3.4, 5.5, 10.1, 13.3 · liquefaction energy · kWh per kg H₂
0
2
4
6
8
10
12
14
16
kWh per kg H₂
Linde-Hampson cycle
10–15
Claude cycle
7–10
Brayton cycle (pre-cooling)*
6–8*
Commercial plants today
10–13
Linde Leuna, reported
11.9
Kawasaki, current development
8–9
Kawasaki, large-scale target
6
Unreachable: below the minimum work to liquefy, 3.3 kWh/kg (dashed) or 3.9 with ortho-para conversion
*Brayton is a pre-cooling cycle inside integrated plants, so its figure is not directly comparable with the other cycles. Most commercial plants use modified Claude cycles with pre-cooling, expansion turbines and staged ortho-para conversion. Minimum work: US DOE Hydrogen Program Record 9013 (2009), as cited in Section 13.3.
Notes: Linde-Hampson is simple but energy hungry; Claude adds expansion turbines; Brayton is used for pre-cooling. Most commercial plants run modified Claude cycles. The shaded zone cannot be reached by any liquefier.

## Slide 5: Five companies lead LH₂ technology, and Kawasaki is the only one offering the full chain from liquefier to receiving terminal
LiqH₂VC Database Rev 0 · Sections 4 and 10 · technology players
Linde
Munich, Germany
Claude-cycle liquefiers, heat exchangers, compressors, storage
Leuna, Germany: 5 to 10 t/day
La Porte, Texas: over 30 t/day
LH₂ supply to NASA
Air Liquide
Paris, France
Helium-cycle liquefiers and full cryogenic equipment
North Las Vegas: 30 t/day
South Korea: 90 t/day, world's largest
Wenchang, China: 1,500 L/h
Chart Industries (Baker Hughes)
Georgia, USA
Cold boxes, turboexpanders, heat exchangers, modular plants
Two 15 t/day plants for Plug Power
Standard plants of 5–30 t/day
Kawasaki Heavy Industries
Tokyo, Japan
Liquefiers, cryogenic tanks, LH₂ carriers, receiving terminals
HESC Australia–Japan chain
Suiso Frontier, 1,250 m³ carrier
Hy touch Kobe terminal
40,000 m³ carrier by 2030
Plug Power
New York, USA
In-house liquefaction with PEM electrolysis and trailer logistics
Woodbine, Georgia: 15–17.5 t/day
Graham, Texas: 45 t/day design
Alabama, NY: 74 t/day target
Full chain
Capacities as stated in each company profile (Section 4); Section 10 notes Kawasaki is currently the single player covering liquefaction, shipping, receiving and regasification.
Notes: Linde and Air Liquide build the largest liquefiers; Chart supplies equipment; Plug Power integrates electrolysis and liquefaction; Kawasaki covers liquefaction, ships and terminals.

## Slide 6: The largest liquefier operating today is 90 t/day at Incheon; Kawasaki's planned 115 t/day train would be bigger than any plant built
LiqH₂VC Database Rev 0 · Sections 5 and 10.1 · liquefaction capacity · t/day LH₂
Chart: 
| Chiba, JP · Iwatani · 2009 | Akashi, JP · Kawasaki · 2014 | Osaka, JP · Iwatani · 2006 | Yamaguchi, JP · Iwatani, Tokuyama · 2017 | Leuna, DE · Linde · 2021 | Woodbine, US · Plug Power · 2024 | La Porte, US · Air Products & Praxair · 2021 | Las Vegas, US · Air Liquide · 2022 | Ulsan, KR · Hyosung–Linde · 2024 | Incheon, KR · SK E&S, Air Liquide · 2024 | Kawasaki unit train (planned)
Capacity, t/day | 5 | 5 | 10 | 10 | 10 | 17.5 | 27.2 | 27.2 | 35.6 | 90 | 115
90 t/day
Incheon, three 30 t/day trains, completed May 2024
115 t/day
Kawasaki's design train size per liquefier
11.9 kWh/kg
Reported energy use at Linde Leuna
Woodbine shown at the top of its 15–17.5 t/day range. Sources disagree within the database: Las Vegas is 27.2 t/day in Table 5.6 but 30 t/day in Section 5.4, and La Porte is 27.2 t/day in Table 5.6 but over 30 t/day in Section 4.1.
Notes: Most plants built in the last 20 years are 5 to 35 t/day. Incheon (SK E&S, Air Liquide equipment) is three 30 t/day trains. The dark bar is Kawasaki's design train, not a built plant.

## Slide 7: Large double-wall vacuum-insulated tanks lose about 0.1 % of their LH₂ a day, and the boil-off has to be vented, used or re-liquefied
LiqH₂VC Database Rev 0 · Sections 6 and 8.2 · LH₂ storage · boil-off in % of tank contents per day
Double-wall vacuum-insulated LH₂ tank (Linde, Figure 7)
Boil-off options: vent it, compress it, re-liquefy it, or stop it with active zero-boil-off refrigeration.
Large stationary tanks
Plants and terminals. Lowest boil-off per tonne; high CAPEX and footprint
Transport tanks
Road, rail and ships. Flexible; more heat ingress, boil-off to manage
Small and medium tanks
Refuelling stations and buffers. Low investment; higher relative losses
Pressurised LH₂ tanks
Higher delivery pressure, less compression; tougher design and safety
~0.07 %/day
NASA Kennedy 3,000 m³ sphere, the largest LH₂ tank in use
≤0.1 %/day
Kawasaki 11,200 m³ design target
0.1 %/day
Database planning value (S&P input, likely conservative)
Boil-off depends on tank size, insulation, storage time and fill level; sloshing, stratification and ortho-para conversion add to it (Section 6.3).
Notes: Bigger tanks lose less per tonne because of their smaller surface-to-volume ratio. 0.1 %/day is the planning value used across the database.

## Slide 8: Only a 1,250 m³ demonstration carrier has sailed; the commercial design is 160,000 m³, 128 times larger
LiqH₂VC Database Rev 0 · Sections 7 and 10.3 · LH₂ carriers · cargo capacity in m³
Suiso Frontier (Kawasaki): 116 m long, 1,250 m³ (~75 t LH₂), 13 knots, about 8,000 gross tonnes. First international LH₂ voyage in 2022.
Chart: 
| Suiso Frontier (sailing) | KHI–JSE carrier (contracted) | Commercial design (target)
Cargo capacity, m³ | 1250 | 40000 | 160000
Mode | Best suited to | Main limits
Road | Regional distribution, refuelling stations, smaller deliveries | Lower capacity; higher cost per kg over long distances
Rail | Larger volumes over longer inland distances | Needs rail infrastructure and dedicated handling
Marine | Large-scale, long-distance and international supply | High ship and terminal CAPEX; boil-off management
Road and rail all use vacuum-insulated cryogenic tanks; mode choice depends on distance, volume, delivery frequency, infrastructure, boil-off and cost (Section 7.3).
Notes: Suiso Frontier proved the concept in 2022. The 40,000 m3 carrier was contracted in January 2026 with an ocean-going demonstration targeted by FY2030. 128x is 160,000 divided by 1,250.

## Slide 9: Kawasaki's specification is the chain's design basis: 8–9 kWh/kg to liquefy, 0.1 %/day boil-off in tanks and 0.2 %/day at sea
LiqH₂VC Database Rev 0 · Section 10 · KHI technical specification
Liquefier
Export terminal
LH₂ carrier
Import & regasification
115 t/day per train
8–9 kWh/kg H₂ now; 6 at large scale, gains expected 2035–2040
H₂ Claude cycle with N₂ pre-cooling
Iron-based ortho-para catalyst inside the liquefier
Minimum economic scale ~10,000 tpa
Up to 4,000 t (~56,000 m³) per tank, not yet built
Boil-off 0.1 %/day
Boil-off re-liquefied at 8 kWh/kg
Jetty and loading arms costed on an LNG basis
160,000 m³ commercial design; 40,000 m³ being built
29.6 km/h (about 16 knots)
Boil-off 0.2 %/day, burned in a dual-fuel engine
No onboard re-liquefaction
1.30 % vaporised at loading, 1.25 % at unloading
65,000 m³ tanks, boil-off 0.1 %/day
Open-rack vaporiser using seawater
3.8 MJ/kg of heat from seawater, not counted as purchased energy
Ship-to-ship transfer and floating storage not yet considered
Source: Kawasaki questionnaire reply and supplemental information, as recorded in Section 10. Export-terminal CAPEX factors are in Section 8.2.
Notes: These are the values the rest of the database and Section 13 build on. The ship's dual-fuel engine is still in development, so the 0.2 %/day burned as fuel is not yet proven.

## Slide 10: Export-facility cost is a Class 5 estimate (±30–50 %): the liquefier dominates, and its power use should fall from ~10 to ~6 kWh/kg
LiqH₂VC Database Rev 0 · Sections 8 and 10.1–10.2 · export-facility CAPEX inputs · USD, cost year not stated
H₂ liquefier (largest item)
2,250 kUSD per t/day at 30 t/day · scaling exponent −0.38 · fixed O&M 4 %/yr, power extra
LH₂ storage tanks
24 USD/kg LH₂ (steel sphere ×2.5 for insulation and installation) · scaling factor 0.6
Boil-off re-liquefaction
30 MUSD for a 6 t/day unit · scaling factor 0.85 · 8 kWh/kg, to be confirmed
Jetty and cryogenic loading arms
15,960 USD per m³/h of loading rate (LNG benchmark +20 % for LH₂)
Adders on the subtotal
+25 % utilities and civil · +20 % indirects and contingency · ×0.85 India · O&M 2.5 %/yr
Liquefier CAPEX per t/day of capacity, kUSD
Chart: 
| 30 t/day | 60 t/day | 115 t/day | 200 t/day | 300 t/day
kUSD per t/day | 2250 | 1730 | 1350 | 1090 | 940
Computed with the Section 10.1 rule: 2,250 × (size ÷ 30)^−0.38, rounded to 10. 115 t/day = one Kawasaki train.
10 → 6 kWh/kg
Liquefier power use today and as plants grow (Section 8.1, Figure 10)
Tank cost reference size is still ‘xx m³’ in Section 10.2. Storage is sized from plant output, ship size and calls a year (6 loadings a year, 5 % minimum heel assumed).
Notes: No LH2 export terminal has been built at this scale, hence the wide range. The chart applies the database's own scaling rule to show why bigger liquefiers are cheaper per tonne.

## Slide 11: There is no dedicated LH₂ regulation yet: Japan has approved projects case by case, so a permitting timeline cannot be set
LiqH₂VC Database Rev 0 · Section 11 · regulatory compliance
What exists today
Japan: project elements not covered by existing rules were reviewed and approved by a special evaluation committee
Elsewhere: a similar country-by-country approach may follow, but this is not confirmed
Not yet identified in the sources reviewed
×
Classification-society rules or Approval in Principle for LH₂ carriers
×
Classification of ship cargo tanks
×
Design and safety standards for liquefiers, ships and terminals
×
Carbon-border or emissions-reporting requirements
?
Carbon-intensity disclosure for the liquefier: needs a feasibility study, as it varies with plant size
Notes: Regulation is an open item for any LH2 project outside Japan. Each gap below is something we would need to resolve before committing to a schedule.

## Slide 12: Two challenges dominate: liquefying 100,000 t a year needs about 103 MW non-stop, and ship boil-off is still unproven at full scale
LiqH₂VC Database Rev 0 · Section 12 · key challenges
103 MW
of power running all the time, just to liquefy 100,000 t of hydrogen a year. Finding that much low-carbon power at a low price is critical.
0.2 vs ~3.4 %/day
Planned ship boil-off against rates reported in smaller-scale Suiso Frontier studies. No full-scale vessel data yet; one voyage vented significant hydrogen.
Other challenges
1
Bigger ships cost more
Only a demo ship has sailed; large cargo tanks are hard to build; ship price not shared
2
Costs are still unclear
Liquefaction and regas cost per kg not shared; needs a feasibility study
3
Rules and permits uncertain
Case by case so far, mainly in Japan (see previous slide)
4
Materials and safety need detail
Cargo-tank metal not confirmed; likely needs a bigger safety zone than ammonia
Notes: 103 MW is liquefaction only, at 8-9 kWh/kg; producing the hydrogen is extra. The 3.4 %/day figure comes from small-scale Suiso Frontier studies and is a reference value, not project data.

## Slide 13: LH₂ and NH₃ are compared on the same job: one 40,000 m³ cargo, from hydrogen gas at the export plant to hydrogen gas at the import terminal
LiqH₂VC Database Rev 0 · Section 13.1 · basis of the LH₂ vs NH₃ comparison
LH₂ route
2,832 t of H₂ per cargo
Prepare cargo
Liquefier, 9 kWh/kg H₂
Export tank
Boil-off 0.1 %/day, re-liquefied
Voyage, 20 days
Boil-off 0.40 %/day burned as engine fuel
Import terminal
Seawater vaporiser, 3.8 MJ/kg of free heat
NH₃ route
27,280 t of NH₃ = 4,871 t of H₂
Prepare cargo
Haber-Bosch, 1 kWh/kg H₂ (team input)
Export tank
Boil-off 0.05 %/day, re-liquefied
Voyage, 20 days
Boil-off 0.15 %/day re-liquefied; ammonia bought as fuel
Import terminal
Cracker: 6.5 kg NH₃ per kg H₂ gas-fired, 7.2 clean fuel
Both export tanks 60,000 m³ with 5 days per cargo. Energy on a lower-heating-value basis; electricity as delivered kWh. Chosen values: 20 sea days, tank size and storage time, 3.94 kWh/kg to re-liquefy LH₂ boil-off. Several NH₃ values are team inputs or estimates that still need sources.
Notes: Same ship size, same distance, same end product. The NH3 cargo carries 1.72 times more hydrogen, but has to be cracked back at the far end.

## Slide 14: On current inputs, ammonia with a gas-fired cracker uses about 14 % less energy than LH₂: 11.36 against 13.27 kWh/kg of hydrogen delivered
LiqH₂VC Database Rev 0 · Section 13.6 · end-to-end energy · kWh per kg H₂ delivered
Chart: 
| NH₃, clean-fuel cracker · 11.66 | NH₃, gas-fired cracker · 11.36 | LH₂ route · 13.27
Liquefaction or Haber-Bosch | 1.29 | 1.16 | 9.78
Export-tank boil-off | 0.01 | 0.01 | 0.03
Ship fuel bought | 1.8 | 1.63 | 0.51
Cargo H₂ burned as ship fuel | 0 | 0 | 2.9
Regasification or cracking | 8.56 | 8.56 | 0.05
Share of hydrogen delivered
Route | Burned on the way | Delivered
LH₂ | 227 t as ship fuel | 92.0 %
NH₃, gas-fired | 675 t in cracker | 86.2 %
NH₃, clean fuel | 1,083 t in cracker | 77.8 %
Tonnes are per 40,000 m³ cargo (H₂ or H₂ equivalent). NH₃ ship fuel is bought separately, so the NH₃ cargo arrives whole (assumption).
Labels under 0.6 kWh/kg hidden (export-tank boil-off 0.01–0.03; LH₂ ship fuel bought 0.51; LH₂ regas 0.05). LH₂ ship boil-off 0.40 %/day; Haber-Bosch 1 kWh/kg H₂ (team input). Totals are 34 % and 40 % of the hydrogen LHV.
Notes: LH2's energy sits upstream in the liquefier; ammonia's sits downstream in the cracker. LH2 delivers more of the hydrogen it starts with.

## Slide 15: LH₂ pays 8.6 kWh/kg more upstream and 1.8 more at sea, then wins back 8.5 downstream because vaporising needs almost no energy
LiqH₂VC Database Rev 0 · Sections 13.2–13.6 · energy by stream, LH₂ against gas-fired NH₃ · kWh per kg H₂ delivered
LH₂ minus NH₃ (gas-fired cracker), kWh/kg H₂
Chart: 
| Upstream | At sea | Downstream | Full chain
LH2 minus NH3 | 8.6 | 1.8 | -8.5 | 1.9
Stream | LH₂ | NH₃ | Difference
Upstream | 9.81 | 1.17 | +8.6
At sea | 3.41 | 1.63 | +1.8
Downstream | 0.05 | 8.56 | −8.5
Full chain | 13.27 | 11.36 | +1.9
Upstream: the liquefier needs about nine times the energy per kg of the ammonia plant
At sea: LH₂ burns 227 t of its own cargo as engine fuel
Downstream: the cracker burns ammonia and natural gas; LH₂ regas uses free seawater heat
Positive = LH₂ uses more energy. At sea includes the cargo hydrogen LH₂ burns. Haber-Bosch power and sea days are still placeholders, so the net figure will move with them.
Notes: Read left to right: the liquefier is LH2's big cost, the cracker is ammonia's. Net, LH2 uses 1.9 kWh/kg more on these inputs.

## Slide 16: The ranking can flip: LH₂ uses the least energy if Haber-Bosch needs more than ~2.65 kWh/kg H₂, or once hydrogen production is counted
LiqH₂VC Database Rev 0 · Sections 13.3, 13.6 and 13.7 · kWh per kg H₂ delivered; supply case 100,000 t H₂ a year
Case | LH₂ | NH₃ gas-fired | NH₃ clean fuel
Default inputs | 13.27 | 11.36 | 11.66
LH₂ ship boil-off 0.2 %/day, not 0.40 | 12.72 | 11.36 | 11.66
Haber-Bosch 2.65 kWh/kg H₂, not 1 | 13.27 | 13.27 | 13.78
Haber-Bosch 3 kWh/kg H₂, not 1 | 13.27 | 13.68 | 14.23
Hydrogen production included (electrolysis 60 kWh/kg) | 78.49 | 81.00 | 88.80
Lowest energy in each case shown in purple.
Delivering 100,000 t of H₂ a year
5 vs 4 ships
40,000 m³ ships for LH₂ against gas-fired NH₃; LH₂ needs 4.97, close to a sixth
108.7 vs 116.1 ktpa
Hydrogen to produce for 100 ktpa delivered (LH₂ against gas-fired NH₃)
152 vs 130 MW
Average chain power, 1,327 against 1,136 GWh a year
Round trip 42.5 days (two 20-day legs, two 1.25-day port calls), 90 % ship availability (assumption), 7.73 voyages per ship a year. The liquefier draws about 112 MW here, against 103 MW in Section 12.1, because it must make 108.7 ktpa.
Notes: Haber-Bosch energy is the swing input: the team value of 1 kWh/kg H2 may exclude the air separation unit. The placeholder range with air separation, 2.8-3.9 kWh/kg H2, is above the break-even.

## Slide 17: On energy cost alone, gas-fired ammonia is cheapest at USD 1.208/kg H₂ against USD 1.754 for LH₂; liquefier power is ~78 % of the LH₂ bill
LiqH₂VC Database Rev 0 · Section 13.8 · energy cost · USD per kg H₂ delivered, cost year not stated
Chart: 
| NH₃, clean-fuel cracker · 1.579 | NH₃, gas-fired cracker · 1.208 | LH₂ route · 1.754
Export plant electricity | 0.181 | 0.163 | 1.374
Marine fuel oil | 0.004 | 0.004 | 0.025
Ammonia fuel | 1.352 | 0.84 | 0
Natural gas | 0 | 0.16 | 0
Import terminal electricity | 0.041 | 0.041 | 0.007
Cargo H₂ burned as ship fuel | 0 | 0 | 0.348
USD 54.5 M a year
Energy-cost gap between LH₂ and gas-fired NH₃ at 100,000 t a year
USD 1.406/kg
LH₂ energy cost even at a hydrogen price of zero, still above gas-fired NH₃
USD 1.99/kg
Hydrogen price below which LH₂ beats the clean-fuel NH₃ route
Prices are team inputs in USD with no cost year: electricity 140 USD/MWh, marine fuel oil 553 USD/t, natural gas 13 USD/MMBtu (LHV), ammonia 700 USD/t; hydrogen 4.00 USD/kg (assumption); import electricity held equal to export (placeholder). Labels under 0.10 hidden.
Notes: Only energy is priced: no capital, charter, port, carbon or hydrogen-feed cost. The hydrogen price only affects LH2, through the cargo it burns.

## Slide 18: Neither carrier wins on every measure: ammonia leads on energy, energy cost and ship count, while LH₂ delivers more of its hydrogen
LiqH₂VC Database Rev 0 · Section 13.9 · summary of the LH₂ vs NH₃ screening
Where LH₂ is ahead
Delivers 92.0 % of the hydrogen it starts with, against 86.2 % and 77.8 % for NH₃
The import terminal only vaporises the liquid: 0.05 kWh/kg, no chemical conversion
Uses the least energy once hydrogen production is counted: 78.49 against 81.00 kWh/kg
Where NH₃ (gas-fired cracker) is ahead
Less energy per kg delivered: 11.36 against 13.27 kWh/kg
Lower energy cost: USD 1.208 against 1.754 per kg
Fewer ships for 100,000 t a year: 4 against 5
Upstream, even a perfect liquefier could not match the ammonia plant
Not yet decided: capital cost, ship cost and shipping economics still need cost data from a full feasibility study.
Notes: This is a screening view of energy and energy cost. The capital-cost and shipping-economics comparison still needs feasibility-study cost data.

## Slide 19: Six open items could change the result; closing them needs supplier and vessel data, the internal ammonia dataset and a feasibility study
LiqH₂VC Database Rev 0 · Sections 10.2, 11, 12.3 and 13.9 · open items
Open item | Current value | Why it matters
Haber-Bosch energy | 1 kWh/kg H₂ (team input) | May exclude air separation. NH₃ stays ahead only below ~2.65 kWh/kg H₂ (2.25 with a clean-fuel cracker)
LH₂ ship boil-off | 0.40 %/day (team input); 0.2 %/day in Section 12.2 | No full-scale data. Each extra 0.1 %/day removes about 2 % of the cargo over 20 sea days
Sea days per cargo | 20 (assumption) | No corridor fixed. Sets ship count and fuel; LH₂ is close to a sixth ship (4.97)
Hydrogen production energy | Not counted; 60 kWh/kg when included (assumption) | Counting it puts LH₂ ahead, because it loses less hydrogen
Other NH₃ values | Re-liquefaction 0.25 kWh/kg, density 682 kg/m³, LHV 18.6 MJ/kg (estimates) | To be replaced with the internal ammonia dataset and the import-terminal power price
Not yet included | — | Plant, ship and terminal CAPEX and OPEX, charter, carbon cost (CO₂, N₂O), safety and permitting
Database-wide gaps also open: LH₂ regulation and permitting (Section 11), liquefaction, regas and ship costs (Section 12.3), and the reference tank size behind 24 USD/kg (Section 10.2).
Notes: These are the inputs to firm up next. The first two matter most for the ranking.

## Slide 20: Questions and discussion
LH2 Value Chain Technology Database, Rev 0